## Slide 1
PRESCRIPTIVE ANALYTICS · PEPPERDINE MSBA
Optimizing California's
NEVI Charging Infrastructure
A Mixed Integer Programming approach to site selection, port allocation,
and equity-weighted optimization under a $10M federal budget constraint.
Team JCT · DESC 605 Midterm · Pepperdine Graziadio
$5B
Federal NEVI
Program
11
Optimal Sites
Selected
168K
ZEVs Covered
(Demand Focus)

## Slide 2
BACKGROUND
The Problem: Where Should California's EV Infrastructure Go?
⚡
$5B in Federal NEVI Funds
The National Electric Vehicle Infrastructure program is actively deploying billions in EV charging investment across all 50 states — site selection decisions are being contested right now.
⚖️
Equity vs. Efficiency Conflict
Justice40 policy mandates ≥40% of federal climate investment reaches disadvantaged communities (DACs). Purely efficiency-driven models underserve these areas.
📍
No Systematic Siting Framework
Current decisions rely on ad hoc criteria. California needs a data-driven, reproducible model that balances population coverage, EV demand, and equity obligations simultaneously.

## Slide 3
DATA
Data Sources & Candidate Sites
Dataset | Source | Role in Model
NEVI Candidate Sites | CA Energy Commission | 400 pre-screened highway-adjacent locations
ZEV Registration Data | CA DMV | Estimated EV demand per candidate site
CalEnviroScreen 4.0 (CES) | OEHHA / CalEPA | Disadvantaged community (DAC) classification
US Census ACS | U.S. Census Bureau | Population density by census tract
NEVI Federal Standards | FHWA | Port count constraints (4–12 per site)
Cost Assumptions | DOE / Industry benchmarks | Infrastructure cost per site and port
→ 400 candidate sites evaluated · 11 selected by optimizer · 89 months of historical EV data

## Slide 4
METHODOLOGY
Analytical Framework: Three-Layer Approach
01
Descriptive Analytics
Regression analysis of 89 months of EV registration data. Identified time trend, COVID-19 disruption, and seasonal demand patterns. Key finding: population alone is a weak predictor of EV adoption (R² = 0.008).
02
Predictive Analytics
Multiple linear regression with month index, COVID indicator, and seasonal dummies. Applied to all 400 candidate sites to estimate forward-looking ZEV demand and site-level coverage potential.
03
Prescriptive Analytics (MIP)
Mixed Integer Programming model determines binary site selection (y) and integer port allocation (x) across three strategic weight configurations. Optimizes infrastructure impact within hard budget and policy constraints.

## Slide 5
MODEL
Optimization Model: MIP Formulation
DECISION VARIABLES
yᵢ ∈ {0,1} — binary: site i selected? xᵢ ∈ ℤ⁺ — integer: ports at site i
OBJECTIVE FUNCTION
Maximize:
Utility = (Population × w₁) + (ZEV Demand × w₂) + (Equity Score × w₃)
Weights adjust per strategy to model three distinct planning philosophies.
KEY CONSTRAINTS
Budget
Total infrastructure cost ≤ $10M
Justice40 / DAC
≥ 40% of investment in disadvantaged communities
NEVI Standards
Each selected site: 4–12 charging ports
Binary Logic
Ports only installed at selected sites (xᵢ ≤ M·yᵢ)
Non-negativity
All decision variables ≥ 0

## Slide 6
ANALYSIS
Statistical Analysis: What Drives EV Demand?
R² = 0.849
CCRN model fit
R² = 0.008
Population → EV adoption
p < 0.001
Time trend significance
KEY FINDINGS FROM REGRESSION
↗
Time trend is the strongest predictor — EV adoption is growing consistently month-over-month, independent of population size.
⚠
Population is a poor proxy for EV demand (R² = 0.008). Infrastructure planned on population density alone will systematically misallocate resources.
🦠
COVID-19 created a structural break in CCRN demand (significant positive coefficient). Seasonal dummies capture winter peaks across all qualification types.
✓
Implication: site selection must be weighted by observed ZEV registration data, not census population — which our MIP model enforces.

## Slide 7
STRATEGY DESIGN
Three Optimization Strategies
Strategy A
Population Focus
Maximize geographic reach
w₁ = 0.8 | w₂ = 0.1 | w₃ = 0.1
Prioritizes census population density. Sites selected where the most people live — not necessarily where EVs are or where underserved communities need infrastructure.
Strategy B
Demand Focus
Maximize EV coverage efficiency
w₁ = 0.1 | w₂ = 0.8 | w₃ = 0.1
Prioritizes existing ZEV registration density. Concentrates chargers where EVs already operate — producing the highest ROI per site and maximum ZEV coverage within budget.
Strategy C
Equity Baseline
Justice40-weighted allocation
w₁ = 0.1 | w₂ = 0.1 | w₃ = 0.8
Strongly prioritizes disadvantaged community (DAC) score. Ensures federal equity obligations are exceeded while still satisfying all budget and NEVI port-count constraints.

## Slide 8
RESULTS
Optimization Results: All Strategies
Chart: Total Budget Spent ($10M Cap)
| Population Focus | Demand Focus | Equity Baseline
Total Cost ($M) | 9.95 | 9.95 | 9.95
Chart: Strategic Performance (ZEV Coverage)
| Population Focus | Demand Focus | Equity Baseline
ZEV Coverage | 46399 | 168751 | 99505

## Slide 9
KEY FINDING
Strategy Comparison Scorecard
Metric | Strategy A Population Focus | Strategy B Demand Focus ★ | Strategy C Equity Baseline
Sites Selected | 11 | 11 | 11
Total Budget Used | $9.95M | $9.95M | $9.95M
DAC Investment % | 40.2% | 40.2% | 40.2%
ZEV Coverage | 46,399 | 168,751 ✓ | 99,505
ZEV Efficiency (per site) | 4,218 | 15,341 ✓ | 9,045
Justice40 Compliant? | Yes | Yes | Yes
Budget Efficiency | Low | High ✓ | Medium
Recommended? | — | YES ★ | Backup

## Slide 10
EFFICIENCY ANALYSIS
Why Demand Focus Wins: ROI per Site
Chart: Avg ZEVs Covered Per Site
| Population Focus | Demand Focus | Equity Baseline
Avg ZEVs Covered Per Site | 4218 | 15341 | 9045
KEY INSIGHT
3.6×
more ZEVs served per site
under Demand Focus vs.
Population Focus
Same $9.95M budget.
Same 11 sites.
Same DAC compliance.
Radically different outcomes.

## Slide 11
SENSITIVITY
Budget Sensitivity: Coverage Saturation Check
Chart: Total ZEV Coverage vs. Budget (Demand Focus)
| $8M | $10M | $12M | $20M | $30M
ZEV Coverage | 135667 | 168751 | 201031 | 297482 | 401410
$10M
Current Proposal
168,751 ZEVs covered — strong return within federal allocation.
+19%
at $12M budget
Coverage rises to 201K ZEVs — marginal $2M yields meaningful gains.
Linear
no saturation yet
Coverage scales linearly up to $30M+. No diminishing returns in sight at current candidate pool.

## Slide 12
GEOGRAPHIC
Geographic Results: Site Distribution Across California
[ MACRO MAP ]
Statewide view — all 11 sites
across CA (strategy clusters visible)
Screenshot: statewide Folium map
(Population / Demand / Equity overlaid)
[ MICRO MAP — LA CLUSTER ]
Zoomed LA metro — Inglewood/Culver City
cluster + Irvine outlier, tooltips visible
Site: Airport Marina Ford · Ports: 4 · DAC: No
Site: Irvine Spectrum · Ports: 7 · DAC: Yes
All 11 selected sites satisfy NEVI 4–12 port standard · DAC ≥ 40.2% · Budget utilization = 99.5%

## Slide 13
INSIGHTS
Managerial Insights for Policy Makers
1
Adopt Demand-Focused Siting as the Default
The Demand Focus strategy delivers 3.6× more ZEVs served per site at identical cost. Population-weighted siting — the intuitive default — leaves 122,000+ potential EV users without nearby infrastructure.
2
Equity and Efficiency Are Not in Conflict
All three strategies cleared the 40% DAC investment threshold. The Justice40 constraint is binding but not costly — planners can meet federal equity obligations without sacrificing ZEV coverage.
3
Population Is a Misleading Siting Proxy
Regression confirms R² = 0.008 for population predicting EV adoption. Infrastructure policy built on demographic density will systematically underfund areas with high actual EV demand.
4
Budget Increases Yield Linear Returns — Advocate for More
Sensitivity analysis shows no saturation at $30M+. Each incremental $2M in NEVI allocation produces proportional ZEV coverage gains. California should pursue expanded federal allocation.

## Slide 14
CONCLUSION
Recommendation:
Demand-Focused Strategy
Maximizes EV coverage (168,751 ZEVs)
Meets Justice40 / DAC mandate (40.2%)
Optimizes federal investment efficiency
Scales linearly with budget increases
Reproducible via open-source MIP model
Future work: integrate real-time traffic flows, update with 2025 EV registration data, and extend model to multi-year phased deployment.
11
Sites Selected
$9.95M
Budget Utilized
168,751
ZEVs Covered
Cayden Campbell · Team JCT · DESC 605 · Pepperdine MSBA 2025–26